## Slide 1: Summary of MAC Address policy contribution to IEEE 802.11
Antonio de la Oliva (IDCC, UC3M)
Roger Marks (EthAirNet Associates)

## Slide 2: Main ideas
Define ANQP element to transport information on the kind of addressing supporting by the network
Define Beacon element to transport information on the kind of addressing supported by the network

## Slide 3: ANQP element
 | Info ID | Length | MAC Address Policy | Policy Flags | MAC Address Prefix Bytes
Octets: | 2 | 2 | 1 | 1 | 0–6
Bit 0, when set to 1, represents the support of EUI addresses, as specified in IEEE Std 802.
Bit 1, when set to 1, represents the support of ELI addresses, as specified in IEEE Std 802, incorporating IEEE Std 802c-2017.
Bit 2, when set to 1, represents the support of SAI addresses, as specified in IEEE Std 802, incorporating IEEE Std 802c-2017.
Bit 3, when set to 1, indicates the availability of a Local Adddress Assignment Protocol (LAAP) server, per IEEE Std 802.1CQ. The LAAP protocol will provide the STA with a local MAC address assignment or a set of allowed local MAC address assignments.
Bit 4, when set to 1, indicates support for self-assignment, using the MAC address prefix specified in the MAC Address Prefix field. This indicates support for local addresses formed by extending the MAC address prefix to 48 bits.
Bit 5 indicates that specific MAC addresses pre-configured by the administrator are supported.
Bits 6-7 are reserved.
Bitmap value | Description
Bit 0 (MSB) | EUI-48 supported
Bit 1 | ELI-48 supported
Bit 2 | SAI-48 supported
Bit 3 | LAAP Server assignment
Bit 4 | Self-Assignment using specified MAC Address Prefix
Bit 5 | Pre-configured administered address
Bit 6 | Reserved
Bit 7 | Reserved

## Slide 4: Policy Flags
 | B0 B2 |  | B3 B5 | B6 B7
 | Length of MAC Address Prefix subfield (bytes) |  | Prefix Trim subfield (bits) | Reserved
Bits: |  | 3 | 3 | 2
The Length of MAC Address Prefix Bytes subfield is a subfield of 3 bits. When the Length of MAC Address Prefix subfield is set to one of the values of 1–6, that value indicates the length (in octets) of the MAC Address Prefix Bytes field. The Length of MAC Address Prefix Bytes subfield is not set to 0 or 7; those values are reserved.
The Prefix Trim subfield is a subfield of 3 bits and takes one of the values of 0–7, that value indicating number of bits to be truncated from the end of the MAC Address Prefix subfield in order to obtain the MAC Address Prefix. In other words, the MAC Address Prefix is represented as the value of the MAC Address Prefix Bytes field after truncation of some of the most significant bits of the last octet, with the number of truncated bits equal to the value of the Prefix Trim subfield. The bit and octet ordering of the MAC Address Prefix is per Figure 9-1 (Representation of a 48-bit MAC address).

## Slide 5: Beacon Element
 | Element ID | Length | Element ID Extension | MAC Address Policy
Same information as the ANQP Element
Do not contain the MAC range, in order to reduce the size of the beacon